PRODUCT INFORMATION SHEET

OXOSAN FOAM

FOAMING CLEANER & DEGREASER

PRODUCT INFORMATION:

A concentrated liquid detergent designed for use through foaming equipment to remain on surfaces to promote soil suspension & emulsification to cut through grease, fats & organic matter in abattoirs, meat plants or any industrial food processing area. Not suitable for galvanised metal, zinc, aluminium, aluminium alloys or painted surfaces.

_________________________________________________________

ADVANTAGES:

HIGHLY CONCENTRATED:	OxoSan Foam contains powerful alkaline grease cutting  agents  which quickly dissolves animal & vegetable fats, blood & proteins, grease, & organic matter as well as removing bacteria, fungi & algae.

HIGH FOAM STABILITY:	OxoSan Foam produces a stable high foam giving long contact time to promote soil removal.

DEODORISES:	Quickly clears offensive odours

EASY TO RINSE:	Easily rinsed away leaving a clean protein free surface clear of any streaks or stains.

BIODEGRADABLE:	Fully biodegradable.

SOLUBILITY:	100% soluble in water.

___________________________________________________________

DIRECTIONS FOR USE:

With foam generating equipment use at the following concentrations. For walls/floors and alkaline safe surfaces use 1 part detergent with 10 parts water or 3 - 5% depending on the degree of soiling. On stainless steel surfaces use 1 part detergent with 20 parts water. Allow up to 20 minutes contact time & rinse off with clean water using a pressure lance.  Do not mix with other cleaners, particularly acid based cleaners

____________________________________________________________

PACKAGING:

All our plastic drums are high molecular weight; high-density polyethylene designed to bring the product to the customer in perfect conditions.

Size: 5Lt & 20Lt Drums.

____________________________________________________________

QUALITY ASSURANCE:

This product is manufactured in Ireland to ISO 9002 quality standards & conforms to R.E.A.C.H & CLP regulations. Shelf life: Not less than 3 years.

Safety Data Sheet

Corresponding to Regulation (EC) No 1272/2008 (CLP)			Page 1 of 8

Date of issue: 01.01.16						Replaces version of: 01.01.14

PRODUCT NAME: OXOSAN FOAM

SECTION 1: IDENTIFICATION OF THE SUBSTANCE/MIXTURE AND OF THE COMPANY/UNDERTAKING

1.1. Product identifier

Product Name 			OXOSAN FOAM

Product No. 				OIR 621 / KR 323

1.2. Relevant identified uses of the substance or mixture and uses advised against

Identified uses:			Alkaline Cleaning agent

1.3. Details of the supplier of the safety data sheet

Supplier 				Roschem Products Ltd

Windmill Road, Elphin, Co Roscommon, Ireland

Tel: +353 (0)71 9635375	Fax: +353 (0)71 9635414

Email: info@roschemproducts.com

1.4. Emergency telephone number  086 8293845. BEAUMONT HOSPITAL. 01 8379964/66

SECTION 2: HAZARDS IDENTIFICATION

2.1. Classification of the substance or mixture

Classification: 	Regulation (EC) No 1272/2008 H302/H290/314/H335

Human health:  	Harmful if swallowed. Causes severe skin burns and eye damage. May 			cause respiratory irritation

Environment:  	This product contains Sodium Hypochlorite which is toxic to aquatic 			organisms.

2.2. Label elements

Detergent Labelling:  Contains Potassium Hydroxide & Sodium Hypochlorite

Labelling

DANGER		       WARNING

Hazard Statements	H302		Harmful if swallowed

H290 		May be corrosive to metals.

H314 		Causes severe skin burns and eye damage.

H335		May cause respiratory irritation

Precautionary

Statements		P102 		Keep out of the reach of children

P234		Keep only in the original container

P260		Do not breathe mist/vapours/spray

P262		Do not get in eyes, on skin or on clothing

P264		Wash hands thoroughly after handling

P270 		Do not eat, drink or smoke when using this product.

P280		Wear protective gloves & clothing, eye & face protection

P301 & 310	If Swallowed: Rinse out mouth immediately with water. 					Immediately call a poison centre or doctor/physician.

Safety Data Sheet

Corresponding to Regulation (EC) No 1272/2008 (CLP)			Page 2 of 8

Date of issue: 01.01.16						Replaces version of: 01.01.14

P302		IF ON SKIN: Remove contaminated clothing & rinse skin

thoroughly with soap & water. Obtain medical attention if 		irritation persists. Wash contaminated clothing before re-use

P304		If Inhaled: Remove immediately from source to fresh air. 		Obtain medical attention if any discomfort continues.

P305 & 310	IF IN EYES: Flush eyes with water, remove contact lenses if

present and easy to do, continue rinsing. Immediately call a    poison center or doctor/physician.

P390		Absorb spillage to prevent material damage

P501		Dispose of contents/container to in accordance with local 			regulations. Recover, reclaim or recycle, where possible.

2.3. Other hazards	N/A

SECTION 3: COMPOSITION/INFORMATION ON INGREDIENTS

3.2. Mixtures

POTASSIUM HYDROXIDE 10-20% CAS-No.: 1310-58-3 EC No.: 215-181-3

Classification (EC 1272/2008) Classification (67/548/EEC) Skin Corr. 1A - H314 C;R35 Acute Tox. 4 – H302 Xn; R22

SODIUM HYPOCHLORITE SOLUTION. % Cl ACTIVE 1-5% CAS-No.: 7681-52-9 EC No.: 231-668-3

Classification (EC 1272/2008) Classification (67/548/EEC) EUH031 C;R34 Skin Corr. 1B - H314 R31 Aquatic Acute 1 - H400 N;R50

SODIUM XYLENE SULPHONATE 5-15% CAS-No.: 1300-72-7 EC No.:

Classification (EC 1272/2008) Classification (67/548/EEC) Skin Irrit. 2 - H315 Xi;R36/37/38. Eye Irrit. 2 - H319 STOT SE 3 - H335

COCOAMIDOPROPYL BETAINE 5-10% CAS-No.: 61789-40-0 EC No.: 263-058-8

Classification (EC 1272/2008) Classification (67/548/EEC) Eye Dam. 1- H318 Xi: R41.

ALKYL DIMETHYLAMINE OXIDE 1-5% 1-5% CAS-No.: 68955-55-5 EC No.:

Classification (EC 1272/2008) Classification (67/548/EEC) Not Classified Xi;R38,R41. Skin Irrit. 2 - H315 N;R50. Eye Dam. 1 - H318 Aquatic Acute 1 - H400

A Full Text for all R-Phrases and Hazard Statements are Displayed in Section 16

Safety Data Sheet

Corresponding to Regulation (EC) No 1272/2008 (CLP)			Page 3 of 8

Date of issue: 01.01.16						Replaces version of: 01.01.14

SECTION 4: FIRST AID MEASURES

4.1. Description of first aid measures

Inhalation: 	 	Remove immediately from source to fresh air. Obtain medical attention if any discomfort continues.

Skin Contact:	Remove contaminated clothing & rinse skin thoroughly with soap & water. Obtain medical attention if irritation persists.

Eye Contact: 	Flush eyes with water immediately. Obtain medical attention if irritation persists.

Ingestion: 		Rinse out mouth immediately with water. Consult a doctor if irritation persists.

Protection of

first aider:		Avoid ingestion, inhalation & contact with skin and eyes (see Section 8.)

4.2. Most important symptoms and effects, both acute and delayed

Inhalation: 		Spray mists may cause coughing, chest tightness, feeling of chest 				pressure.

Ingestion: 		May cause harm if swallowed. May cause internal injury

Skin contact:		May cause serious chemical burns to the skin.

Eye contact: 		Extreme irritation/damage to eyes & mucous membranes, including 			burning & tearing.

4.3. Indication of any immediate medical attention and special treatment needed

The severity of the symptoms described will vary dependant of the concentration and the length of exposure.

SECTION 5: FIRE FIGHTING MEASURES

5.1 	Suitable Extinguishing Media: 	Water, Foam.

5.2 	Unsuitable: 				N/A

5.3 	Specific Hazards: 		May generate toxic and explosive fumes in a fire.

5.4 	Special Equipment for the

protection of Fire Fighters: 	Fire fighters should wear self-contained breathing apparatus & body protective clothing.

SECTION 6: ACCIDENTAL RELEASE MEASURES

6.1	Personal Precautions: 		Avoid contact with skin and eyes (see Section 8.)

6.2	Environmental Precautions: 		No special measures required

6.3	Methods for Cleaning up: 		Small Spills - Flush with water.

Large Spills - Contain and collect spillage and absorb on to sand.

SECTION 7: HANDLING AND STORAGE

7.1 	Handling

Technical Measures: 		No special measures required.

Safe Handling Advice: 		Avoid contact with eyes & skin. Comply with instructions for use.

7.2	Storage

Technical Measures: 		No special measures required.

Storage Conditions: 		Store in a cool dry place. (See section 10)

Incompatible Products: 	Acids &/or oxidizing agents. Aluminium, brass, tin & zinc are

readily attacked to produce hydrogen gas.

Packaging: 			Plastic Drums.

Packaging Materials: 	Recommended: Plastic Materials, Polyethylene, Polypropylene.

Not Suitable - Uncoated Metal Drums.

Safety Data Sheet

Corresponding to Regulation (EC) No 1272/2008 (CLP)			Page 4 of 8

Date of issue: 01.01.16							Replaces version of: 01.01.14

SECTION 8: EXPOSURE CONTROLS/PERSONAL PROTECTION

8.1. Control parameters:

| Name | STD | Occupational Exposure Limit Value (8-hour reference period) ppm mg/m3 | Occupational Exposure Limit Value (8-hour reference period) ppm mg/m3 | Notes |
| --- | --- | --- | --- | --- |
| POTASSIUM HYDROXIDE | OELV | - |  | - | 2 |  |

OELV = Occupational Exposure Limit Value.

8.2	Personal Protection Equipment:

Respiratory Protection:	Provide adequate ventilation in areas of confined space.

Hand Protection:		Use Chemical Resistant Gloves to EN Standard 374 Level 1, Letter Code K

Eye Protection:		Use Chemical Goggles or Face Shield to EN Standard 166 Level 3 or higher

Skin Protection: 		Wear Plastic Apron EN Standard 13034 Type PB[6] & Face Shield EN Standard 166 Level 3 or higher

8.3	Hygiene Measures:		Handle in accordance with good industrial hygiene and

safety practices.

SECTION 9: PHYSICAL AND CHEMICAL PROPERTIES

9.1. Information on basic physical and chemical properties

Physical State:	Clear Liquid.

Colour:		Colourless/Yellow.

Odour:		Non-objectionable.

Solubility:		100% Soluble in Water.

Flashpoint:		Not Determined

Explosive Properties:	Not Determined

pH:	(100%)		>13

Density:		1.35kg/dm3

SECTION 10: STABILITY AND REACTIVITY

10.1. Reactivity: 	There are no known reactivity hazards associated with this product.

10.2. Chemical stability: 	Stable under normal temperature conditions and recommended use.

10.3. Possibility of hazardous reactions: 		Hazardous Polymerisation N/A

10.4. Conditions to avoid: 	Avoid Extreme Temperatures. Avoid contact with acids &/or oxidising agents.

10.5. Incompatible materials: 	Acids &/or oxidizing agents. Aluminium, brass, tin & zinc produces hydrogen.

10.6. Hazardous decomposition products: 	None under normal conditions.

Safety Data Sheet

Corresponding to Regulation (EC) No 1272/2008 (CLP)			Page 5 of 8

Date of issue: 01.01.16						Replaces version of: 01.01.14

SECTION 11: TOXICOLOGICAL INFORMATION

11.1. Information on toxicological effects:

Inhalation: 	Irritating to respiratory system. Prolonged inhalation of high concentrations may 		damage respiratory system.

Ingestion: 	Causes burns. Swallowing concentrated chemical may cause severe internal 		injury. May cause chemical burns in mouth, esophagus and stomach.

Skin contact: Corrosive and Irritating to skin. Will burn skin on contact

Eye contact: 	Risk of serious damage to eyes. Causes burns. Contact with concentrated 		chemical may very rapidly cause severe eye damage, possibly loss of sight.

11.2.Toxicological information on ingredients:

POTASSIUM HYDROXIDE (CAS: 1310-58-3)

Acute Toxicity (Oral LD50)

333 mg/kg Rat

REACH dossier information

SODIUM HYPOCHLORITE SOLUTION. % Cl ACTIVE (CAS: 7681-52-9)

Acute Toxicity (Oral LD50)

1100 mg/kg Rat

Acute Toxicity (Dermal LD50)

> 20000 mg/kg Rabbit

Acute Toxicity (Inhalation LC50)

> 10.5 mg/l (vapours) Rat 1 hour

REACH dossier information

SODIUM XYLENE SULPHONATE (CAS: 1300-72-7)

Acute Toxicity (Oral LD50)

> 7000 mg/kg Rat

Acute Toxicity (Dermal LD50)

> 2000 mg/kg

REACH dossier information

COCOAMIDOPROPYL BETAINE (CAS: 61789-40-0)

Acute Toxicity (Oral LD50)

4900 mg/kg Rat

IUCLID chemical data sheet.

ALKYL DIMETHYLAMINE OXIDE (CAS: 68955-55-5)

Acute Toxicity (Oral LD50)

> 5000 mg/kg Rat

Acute Toxicity (Dermal LD50)

> 2000 mg/kg Rat

Acute Toxicity (Inhalation LC50)

> 1.6 mg/l (dust/mist) Rat 4 hours

REACH dossier information

SECTION 12: ECOLOGICAL INFORMATION

Eco-toxicity

This product may affect the acidity (pH-factor) in water with risk of harmful effects to aquatic organisms

Safety Data Sheet

Corresponding to Regulation (EC) No 1272/2008 (CLP)			Page 6 of 8

Date of issue: 01.01.16						Replaces version of: 01.01.14

12.1. Toxicity

Ecological information on ingredients:

POTASSIUM HYDROXIDE (CAS: 1310-58-3)

Acute Toxicity - Fish

LC50 24 hours 80 mg/l Various species

Acute Toxicity - Aquatic Invertebrates

EC50 48 hours 30-1000 mg/l Daphnia magna

REACH dossier information

SODIUM HYPOCHLORITE SOLUTION. % Cl ACTIVE (CAS: 7681-52-9)

Acute Toxicity - Fish

LC50 96 hours > .023 mg/l Pink salmon

Acute Toxicity - Aquatic Invertebrates

EC50 48 hours 35 μg/L Ceriodaphnia dubia

NOEC 48 hours 25 μg/L Ceriodaphnia dubia

Acute Toxicity - Aquatic Plants

EC50 96 hours ~ 0.01 mg/l Myriophyllum spicatum

NOEC 96 hours 0.02 mg/l Myriophyllum spicatum

REACH dossier information

SODIUM XYLENE SULPHONATE (CAS: 1300-72-7)

Acute Toxicity - Fish

LC50 96 hours > 1000 mg/l Onchorhynchus mykiss (Rainbow trout)

Acute Toxicity - Aquatic Invertebrates

EC50 48 hours > 1020 mg/l Daphnia magna

Acute Toxicity - Aquatic Plants

EC50 96 hours 758 mg/l Pseudokirchnerella subcapitata

REACH dossier information

COCOAMIDOPROPYL BETAINE (CAS: 61789-40-0)

Acute Toxicity - Fish

LC50 96 hours 2 mg/l Brachydanio rerio (Zebra Fish)

Acute Toxicity - Aquatic Invertebrates

EC50 48 hours 10.5 mg/l Daphnia magna

Acute Toxicity - Aquatic Plants

EC50 96 hours 0.55 mg/l Scenedesmus subspicatus

IUCLID chemical data sheet.

ALKYL DIMETHYLAMINE OXIDE (CAS: 68955-55-5)

Acute Toxicity - Fish

LC50 96 hours 0.59 mg/l Pleuronectes platessa

Acute Toxicity - Aquatic Invertebrates

EC50 48 hours 0.14 mg/l Daphnia magna

Acute Toxicity - Aquatic Plants

EC50 72 hours 0.75 mg/l Selenastrum capricornutum

REACH dossier information

12.2. Persistence and degradability

ALKYL DIMETHYLAMINE OXIDE (CAS: 68955-55-5)

Biodegradation

Activated sludge Degradation (72%) 28 days

REACH dossier information. The substance is readily biodegradable

Safety Data Sheet

Corresponding to Regulation (EC) No 1272/2008 (CLP)			Page 7 of 8

Date of issue: 01.01.16						Replaces version of: 01.01.14

Degradability: 	The surfactant(s) contained in this preparation comply with the biodegradability criteria as laid down in Regulation (EC) No.648/2004 on detergents. Data to support this assertion are held at the disposal of the competent authorities of the Member States and will be made available to them, at their direct request or at the request of a detergent manufacturer.

12.3. Bioaccumulative potential

POTASSIUM HYDROXIDE (CAS: 1310-58-3)

Not relevant, does not bioaccumulate

ALKYL DIMETHYLAMINE OXIDE (CAS: 68955-55-5)

Bioaccumulation factor

BCF 12.7 Pimephales promelas (Fat-head Minnow)

REACH dossier information

12.4. Mobility in soil

Mobility: 	The product is soluble in water.

12.5. Results of PBT and vPvB assessment

Not identified as a PBT or vPvB substance.

12.6. Other adverse effects

Not determined.

SECTION 13: DISPOSAL CONSIDERATIONS

General information: 	Waste to be treated as controlled waste. Disposal to licensed waste disposal site in accordance with local Waste Disposal Authority

13.1. Waste treatment methods

Dispose of waste in accordance with local regulations. Recover, reclaim or recycle, where possible.

SECTION 14: TRANSPORT INFORMATION

The product is not covered by international regulation on the transport of dangerous goods:

REGULATIONS			CLASS

RID/ADR:			8

ICAO/IATA-DGR:			8 UN 1719

GGVSee/IMDG-Code:	8 / 80

14.1. UN number

UN 1719

14.2. UN proper shipping name

Caustic Alkali Liquid NOS

14.3. Transport hazard class(es)

N/A

14.4. Packing Group

III

14.5. Environmental Hazards

Environmentally Hazardous Substance/Marine Pollutant: N/A

14.6. Special precautions for user

NA

14.7. Transport in bulk according to Annex II of MARPOL73/78 and the IBC Code

N/A

Safety Data Sheet

Corresponding to Regulation (EC) No 1272/2008 (CLP)			Page 8 of 8

Date of issue: 01.01.16						Replaces version of: 01.01.14

SECTION 15: REGULATORY INFORMATION

15.1. Safety, health and environmental regulations/legislation specific for the substance or mixture

Statutory Instruments

Corresponding to Preparations Regulations S.I. No. 62 of 2004

Approved Code Of Practice

Classification and Labelling of Substances and Preparations Dangerous for Supply.

6 / 7

Guidance Notes

Workplace Exposure Limits EH40.

EU Legislation

Regulation (EC) No 1272/2008 of the European Parliament and of the Council of 16 December 2008 on Classification, Labelling and Packaging of substances and mixtures, amending and repealing Directives 67/548/EEC and 1999/45/EC, and amending Regulation (EC) No 1907/2006 with amendments (REACH)

15.2. Chemical Safety Assessment

No chemical safety assessment has been carried out.

SECTION 16:	OTHER INFORMATION

Revision Comments

Re-issued according to Regulation (EU) No 453/2010.

Revision Date: 		01.01.16

Revision No: 		3

Replaces version of: 	01.01.14

Risk Phrases In Full

R22		Harmful if swallowed

R31 		Contact with acids liberates toxic gas.

R35 		Causes severe Burns

R50		Very toxic to aquatic organisms

Hazard Statements In Full

H302		Harmful if swallowed

H290 		May be corrosive to metals.

H314 		Causes severe skin burns and eye damage.

H335		May cause respiratory irritation.

__________________________________________________________________________

The information contained herein is based on the present state of our knowledge and is intended to describe our products from the point of view of safety requirements. It should therefore not be construed as guaranteeing specific properties.