PRODUCT INFORMATION SHEET

SC5 GLASS & STAINLESS STEEL CLEANER (RTU)

PRODUCT INFORMATION:

High performance glass & stainless steel cleaner is specially blended with low foaming detergents to cut through film, haze, smudges, dirt, greasy soot & other industrial soils to leave a streak free finish

_________________________________________________________

ADVANTAGES:

GENERAL PURPOSE 	Glass & Stainless Steel Cleaner is a concentrated product effective on APPLICATION:		many surfaces such as stainless steel, chrome, plastic, computer 						keyboards, glass screens, ceramic, porcelain & mirrors.

EFFECTIVE SOIL 		Contains alcohol to evaporate quickly & cut through film, haze, smudges, REMOVAL: 			dirt, grease & other soils both on the inside & outside of buildings.

NON-STREAKING:		Glass & Stainless Steel Cleaner leaves a clear, sparking, streak and 					stain free surface without leaving a film.

NON-FOAMING:		This makes Glass & Stainless Steel Cleaner particularly suitable for 					industrial and institutional cleaning-in-place-systems.

BIODEGRADABLE:		Readily biodegradable water based cleaner.

___________________________________________________________

DIRECTIONS FOR USE:

Turn nozzle to ‘ON’ position & keep bottle in an upright position. Simply spray onto surface from a distance of 20-25 cm before wiping from the surface using a clean, lint free cloth.

____________________________________________________________

HEALTH AND SAFETY: See Safety Data Sheet.

____________________________________________________________

PACKAGING:

All our plastic drums are high molecular weight; high-density polyethylene designed to bring the product to the customer in perfect conditions.

Size: Diluted from 2Lt concentration @ 20mls to 730mls potable water into 750ml Trigger Spray Bottle

___________________________________________________________

QUALITY ASSURANCE:

This product is manufactured in Ireland to ISO 9002 quality standards & conforms to R.E.A.C.H & CLP regulations. Shelf life: Not less than 48 hours.

Safety Data Sheet

Corresponding to Regulation (EC) No 1272/2008 (CLP)				Page 1 of 7

Date of issue: 01.01.17						Replaces version of: 01.01.15

PRODUCT NAME: SC5 GLASS & STAINLESS STEEL CLEANER RTU

SECTION 1: IDENTIFICATION OF THE SUBSTANCE/MIXTURE AND OF THE COMPANY/UNDERTAKING

1.1. Product identifier

Product Name 		SC5 GLASS & STAINLESS STEEL CLEANER RTU

Product No. 			SC 805 750

1.2. Relevant identified uses of the substance or mixture and uses advised against

Identified uses:		Cleaning agent

1.3. Details of the supplier of the safety data sheet

Supplier 			Roschem Products Ltd

Windmill Road, Elphin, Co Roscommon,	Ireland

Tel: +353 (0)71 9635375	Fax: +353 (0)71 9635414

Email: info@roschemproducts.com

1.4. Emergency Contact:  	National Poisons Information Centre, Beaumont Hospital, 					Beaumont Road, Dublin 9. Tel: +353(01)8092566

SECTION 2: HAZARDS IDENTIFICATION

2.1. Classification of the substance or mixture

Classification: 	Regulation (EC) No 1272/2008	Not Classified

Human health:  	Not Classified

Environment:  	This product is Readily Biodegradable and not expected to be hazardous 			to the environment

2.2. Label elements

Detergent Labelling:  		Contains: 	Isopropyl Alcohol

Hazard Phrases 			Not Classified

Precautionary Statements		P102 	Keep out of the reach of children

P301	IF SWALLOWED: Rinse mouth. Call a poison centre 				& 312 	or doctor if you feel unwell & show this label.

2.3. Other hazards	N/A

Safety Data Sheet

Corresponding to Regulation (EC) No 1272/2008 (CLP)				Page 2 of 7

Date of issue: 01.01.17						Replaces version of: 01.01.15

SECTION 3: COMPOSITION/INFORMATION ON INGREDIENTS

3.2. Mixtures

PROPAN-2-OL 1-5% CAS-No.: 67-63-0 EC No.: 200-661-7

Classification (EC 1272/2008) Flam. Liq. 2 - H225 Eye Irrit. 2 - H319 STOT SE 3 - H336

SODIUM XYLENE SULPHONATE <1% CAS-No.: 1300-72-7 EC No.:

Classification (EC 1272/2008) Skin Irrit. 2 - H315 Eye Irrit. 2 - H319 STOT SE 3 - H335

A Full Text for all Hazard Statements are Displayed in Section 16

SECTION 4: FIRST AID MEASURES

4.1. Description of first aid measures

Inhalation: 		In case of inhalation of spray mist: Move person into fresh air and keep at 				rest.

Ingestion: 		DO NOT INDUCE VOMITING! Drink a few glasses of water or milk. Get 				medical attention if any discomfort continues.

Skin contact:		Wash skin with soap and water.

Eye contact:		Promptly wash eyes with plenty of water while lifting the eye lids.

Protection of

first aider:		None noted (see Section 8.)

4.2. Most important symptoms and effects, both acute and delayed

Inhalation: 		No symptoms noted.

Ingestion: 		No specific symptoms noted but may cause discomfort if swallowed

Skin contact:		No specific symptoms noted bur prolonged or excessively exposure may 			cause skin dryness.

Eye contact: 		No specific symptoms noted. But contact may lead to the product 				affecting the natural lubrication of the eye & cause redness &/or tearing

4.3. Indication of any immediate medical attention and special treatment needed

The severity of the symptoms described will vary dependant of the concentration and the length of exposure.

Safety Data Sheet

Corresponding to Regulation (EC) No 1272/2008 (CLP)				Page 3 of 7

Date of issue: 01.01.17						Replaces version of: 01.01.15

SECTION 5: FIRE FIGHTING MEASURES

5.1 	Suitable Extinguishing 		Alcohol-resistant foam, carbon dioxide, dry powder or 	Media:			water fog.

5.2 	Unsuitable: 		Do not use water jet as an extinguisher, as this will spread 			the fire

5.3 	Specific Hazards: 		Avoid breathing fire vapours. Cool containers exposed to 	flames with water until well after the fire is out. Oxides of the 	following substances: Carbon. Vapours are heavier than air 	& may spread near ground & travel a considerable distance 	to a source of ignition & flash back.

5.4 	Special Equipment for the

protection of Fire Fighters: 	Wear full protective clothing & breathing apparatus.

SECTION 6: ACCIDENTAL RELEASE MEASURES

6.1	Personal Precautions: 		Do not smoke, use open fire or other sources of 							ignition. Avoid contact with eyes (see Section 8.)

6.2	Environmental Precautions: 		No special measures required

6.3	Methods for Cleaning up: 		Small Spills - Flush with water.

Large Spills - Contain & collect spillage & absorb on 					to sand.

SECTION 7: HANDLING AND STORAGE

7.1 	Handling

Technical Measures: 			No special measures required.

Safe Handling Advice: 		Avoid contact with eyes. Keep away from heat. Avoid naked flames, sparks and sources of ignition. Comply with instructions for use.

7.2	Storage

Technical Measures: 			No special measures required.

Storage Conditions: 			Store in a cool dry place away from sources of heat or 					ignition

Incompatible Products: 			None known.

Packaging: 				Plastic Drums.

Packaging Materials: 		Recommended: Plastic Materials, Polyethylene, Polypropylene.

Not Suitable - Uncoated Metal Drums.

Safety Data Sheet

Corresponding to Regulation (EC) No 1272/2008 (CLP)				Page 4 of 7

Date of issue: 01.01.17						Replaces version of: 01.01.15

SECTION 8: EXPOSURE CONTROLS/PERSONAL PROTECTION

8.1	Control Parameters.

8.1	Engineering Measures: 	No special measures required.

8.2	Personal Protection Equipment:

Respiratory Protection:	No protection necessary.

Hand Protection:		No protection necessary however if excessive exposure is expected gloves should be worn to avoid skin dryness.

Eye Protection:		No protection necessary however care should be taken to avoid contact with eyes

Skin Protection: 		No protection necessary

8.3	Hygiene Measures:		Handle in accordance with good industrial hygiene and

safety practices

8.4	Occupational Exposure Limits:

| Name | STD | Occupational Exposure Limit Value (8-hour reference period) ppm mg/m3 | Occupational Exposure Limit Value (15 minute reference period) Ppm mg/m3 | Notes |
| --- | --- | --- | --- | --- |
| PROPAN-2-OL | OELV | 200 | - | 400 | - |  |

OELV = Occupational Exposure Limit Value.

SECTION 9: PHYSICAL AND CHEMICAL PROPERTIES

9.1. Information on basic physical and chemical properties

- Appearance: 					Green Liquid.

- Odour:  						Faint Alcohol

- Odour threshold:					N/A

- pH:   						7+/-0.5 (undiluted)

- Melting point / freezing point:			-0.5 to -1°C

- Initial boiling point & boiling range:		No data available

- Flash point:					No data available

- Evaporation rate:					No data available

- Flammability solid, gas:				No data available

- Upper/lower flammability or explosive limits:	No data available

- Vapour pressure:					No data available

- Vapour density:					No data available

- Relative density:					1.00kg/dm3

- Solubility(ies):					Soluble in Water

- Partition coefficient: 	n-octanol/water:		No data available

- Auto-ignition temperature:				No data available

- Decomposition temperature:			No data available

- Viscosity:						No data available

- Explosive properties:				No data available

- Oxidizing properties:				No data available

Safety Data Sheet

Corresponding to Regulation (EC) No 1272/2008 (CLP)				Page 5 of 7

Date of issue: 01.01.17						Replaces version of: 01.01.15

SECTION 10: STABILITY AND REACTIVITY

10.1. Reactivity: 	Strong oxidising agents. Strong acids.

10.2. Chemical stability: 	Stable under normal temperature conditions and recommended use.

10.3. Possibility of hazardous reactions: 		Hazardous Polymerisation N/A

10.4. Conditions to avoid: 	Avoid heat, flames and other sources of ignition. Do not mix with strong acids or oxidising agents

10.5. Incompatible materials: 	None known.

10.6. Hazardous decomposition products: 	None under normal conditions.

SECTION 11: TOXICOLOGICAL INFORMATION

11.1. Information on toxicological effects:

Inhalation: 		No symptoms noted.

Ingestion: 		No specific symptoms noted but may cause discomfort if swallowed

Skin contact:		No specific symptoms noted bur prolonged or excessively exposure may 			cause skin dryness.

Eye contact: 		No specific symptoms noted. But contact may lead to the product 				affecting the natural lubrication of the eye & cause redness &/or tearing.

11.2.Toxicological information on ingredients:

SODIUM XYLENE SULPHONATE (CAS: 1300-72-7)

Acute Toxicity (Oral LD50)

> 7000 mg/kg Rat

Acute Toxicity (Dermal LD50)

> 2000 mg/kg

REACH dossier information

PROPAN-2-OL (CAS: 67-63-0)

Acute Toxicity (Oral LD50)

5.84 g/kg Rat

Acute Toxicity (Dermal LD50)

16.4 mL/kg Rabbit

Acute Toxicity (Inhalation LC50)

> 10000 ppm (vapours) Rat

REACH dossier information

SECTION 12: ECOLOGICAL INFORMATION

Eco-toxicity

Dangerous for the environment if discharged into watercourses. The product is easily biodegradable.

12.1. Toxicity

Ecological information on ingredients:

SODIUM XYLENE SULPHONATE (CAS: 1300-72-7)

Acute Toxicity - Fish

LC50 96 hours > 1000 mg/l Onchorhynchus mykiss (Rainbow trout)

Acute Toxicity - Aquatic Invertebrates

EC50 48 hours > 1020 mg/l Daphnia magna

Acute Toxicity - Aquatic Plants

EC50 96 hours 758 mg/l Pseudokirchnerella subcapitata

REACH dossier information

Safety Data Sheet

Corresponding to Regulation (EC) No 1272/2008 (CLP)				Page 6 of 7

Date of issue: 01.01.17						Replaces version of: 01.01.15

PROPAN-2-OL (CAS: 67-63-0)

Acute Toxicity - Fish

LC50 9640 mg/l Pimephales promelas (Fat-head Minnow)

Acute Toxicity - Aquatic Invertebrates

LC50 24 hours > 10000 mg/l Daphnia magna

Acute Toxicity - Aquatic Plants

Toxicity threshold 168 hours 1800 mg/l Scenedesmus quadricauda

REACH dossier information

12.2. Persistence and degradability

Degradability: 	The surfactant(s) contained in this preparation comply with the biodegradability criteria as laid down in Regulation (EC) No.648/2004 on detergents. Data to support this assertion are held at the disposal of the competent authorities of the Member States and will be made available to them, at their direct request or at the request of a detergent manufacturer.

12.3. Bioaccumulative potential			No data available on bioaccumulation.

12.5. Results of PBT and vPvB assessment	Not determined.

12.6. Other adverse effects			Not determined.

SECTION 13: DISPOSAL CONSIDERATIONS

General information: 	Small amounts (less than 5 Litres) of unwanted product may be flushed with water to sewer. Larger volumes must be sent for disposal to licensed waste disposal site in accordance with local Waste Disposal Authority. Consign empty container to normal waste.

13.1. Waste treatment methods

Dispose of waste in accordance with local regulations. Recover, reclaim or recycle, where possible.

SECTION 14: TRANSPORT INFORMATION

The product is not covered by international regulation on the transport of dangerous goods:

REGULATIONS			CLASS

RID/ADR:			Not Classified

ICAO/IATA-DGR:			Not Classified

GGVSee/IMDG-Code:	Not Classified

14.1. UN number

N/A

14.2. UN proper shipping name

N/A

14.3. Transport hazard class(es)

N/A

14.4. Packing Group

N/A

14.5. Environmental Hazards

Environmentally Hazardous Substance/Marine Pollutant: N/A

14.6. Special precautions for user

NA

14.7. Transport in bulk according to Annex II of MARPOL73/78 and the IBC Code

N/A

Safety Data Sheet

Corresponding to Regulation (EC) No 1272/2008 (CLP)				Page 7 of 7

Date of issue: 01.01.17						Replaces version of: 01.01.15

SECTION 15: REGULATORY INFORMATION

15.1. Safety, health and environmental regulations/legislation specific for the substance or mixture

Statutory Instruments

Corresponding to Preparations Regulations S.I. No. 62 of 2004

Approved Code Of Practice

Classification and Labelling of Substances and Preparations Dangerous for Supply.

Guidance Notes

Occupational Exposure Limits.

EU Legislation

Regulation (EC) No 1272/2008 of the European Parliament and of the Council of 16 December 2008 on classification, labelling and packaging of substances and mixtures, amending and repealing Directives 67/548/EEC and 1999/45/EC, and amending Regulation (EC) No 1907/2006 with amendments.

15.2. Chemical Safety Assessment

No chemical safety assessment has been carried out.

SECTION 16:	OTHER INFORMATION

Revision Comments

Re-issued according to Regulation (EU) No 453/2010.

Revision Date: 		01.01.17

Revision No: 		5

Replaces version of: 	01.01.15

Hazard Statements In Full

H225 	Highly flammable liquid & vapour

H319 	Causes serious eye irritation

H336 	May cause drowsiness or dizziness

H335	May cause respiratory irritation

________________________________________________________________________

The information contained herein is based on the present state of our knowledge and is intended to describe our products from the point of view of safety requirements. It should therefore not be construed as guaranteeing specific properties.